## Slide 1: Milwaukee Tool Tracking Headlamp

## Slide 2: Outline
Problem Statement – Addresses the problem that will be solved in engineering
Solution – The team's approach to solving this problem
Solution Alternatives – Weighing design decisions against alternative methods to solve the same problem
Test Result Summary- Compliance test result
Feras

## Slide 3: Outline
Preliminary Project Specifications – Design requirement specifications made by the customer
Block Diagram – Block diagram of the subsystems and how they interface with each other
Major Subsystems and Specification – The modules chosen to meet design specifications
Integration – what was integrated
Abdullah

## Slide 4: Outline
Price/Cost Analysis – Considerations made in terms of all subsystems design prices
EE 408 Subsystem Test Plan and Results – Summarized outcomes of IMU and Magnetometer test plan and results
Shortcomings and Strengths – What were our best takeaways and what needed improvement
Problems and Risks – Problems we have faced, challenges with integrating subsystems, and risks with development
Matt

## Slide 5
Workers and hobbyists need headlamps to adapt to their work environment and Milwaukee Tool wants to offer tracking and extra features to their existing designs.

## Slide 6: Solution Should satisfy
  Functional requirement
  Material cost expectations
  Deadlines
  Accuracy
  Efficiency of Power

## Slide 7: Solution: A development board was chosen
  Inertial Measurement Unit (IMU) – pitch & yaw
  Magnetometer - yaw
  Servomotors
  Thermistor
  Photocell
  Power System (USB) Port

## Slide 8: Solution Alternatives
Some solutions available that can do the same job
Had to pick based on design requirements from Milwaukee Tool
Solution chosen based on team's evaluation of project timeline and design constraints

## Slide 9: Solution Alternatives
For the tracking subsystem:
1. Camera feedback with microcontroller
2. IMU & Magnetometer with microcontroller
For the servomotors:
1. Servo 1 with plastic gears
2. Servo 2 with carbon fiber gears

## Slide 10: Solution Alternatives
Attributes of Tracking | Camera | IMU & Magnetometer | Attributes of Servomotors | Plastic Gear | Fiber Gear
Material Cost | ~ $ 90.99 | ~ $ 24.98 | Material Cost | ~ $ 6.29 | ~ $ 5.95
Design Cost in Term of Time | Low | High | Design Cost in Term of Time | Equal to option 2 | Equal to option 1
Power Consumption | ~ 1.105 W | ~ 0.0271 W | Power Consumption | ~ 0.20 W | ~ 1.70 W
Possibility | Available | Available | Possibility | Available | Available
Accuracy Test [Within 5%] | Pass | Pass | Accuracy Test [Within 5%] | Pass | Pass
Satisfies Functional Requirements | Yes | Yes | Satisfies Functional Requirements | Yes | Yes

## Slide 11: IMU choices
3 axis accelerometer vs 6 axis IMU
  6 axis IMU has a Gyroscope which will provide more precise results
  Gyroscope has quicker readings
  Simplifies the program

## Slide 12: Tests performed summary
1A) Verify that the device is compatible with a Milwaukee Red LithiumTM Battery Pack, which supplies 3.6V when fully charged. This test will also find the minimum voltage that the circuit still operates (Passed)
1B) Verify that the headlamp will cast a light for at least one-hundred twenty minutes while being powered by an initially fully charged (Spec) battery, which needs further analysis.
1C) Check if the pushbuttons and switches work, which needs further design.
1D) Verify that the LEDs brightness can be controlled by sending a PWM signal based on the lux reading from the ambient light detector (Passed)

## Slide 13: Tests performed summary
2A) Verify that the device will have the ability to direct the light about two axes over a range of 100 degrees in both directions to maintain the illumination of the LED at a fixed direction when tracking is enabled, which needs further design.
2B) Check if the device’s tracking feature will only be available with the White LED mode (Passed)

## Slide 14: Tests performed summary
3A) Verify that when tracking enabled, after no motion is detected for more than 5 minutes, the device enters a low power state, needs further design.
3B) Verify that the total combined leakage current from the battery to the device is less than 1mA when the device is in the low power state, need further design.
4A) Check the mass of the device, which should be less than 300 grams excluding the battery. Also, to check if it is hardhat attachable (Passed)

## Slide 15: Milwaukee Tool Specifications
Powered by a Milwaukee Red Lithium™ Battery Pack
The Headlamp should cast light for120 minutes fully charged
User select auto-brightness
Auto shutdown when overheating
Choose between White and Red (stationary) LEDs
Notes: i. This requires the device to run with a power supply ranging between 3 and 4V
The output brightness will automatically adjust based on ambient light levels

## Slide 16: MILWAUKEE TOOL SPECIFICATIONS
Low state power after 5 minutes of inactivity when the tracking is enabled
Total combined leakage current from the battery to device <1mA in low state power
<300 grams without battery
<20$ bill of materials for tracking feature

## Slide 17: MILWAUKEE TOOL Tracking SPECIFICATIONS
Tracking feature enable/disable button
Direct light 100◦ range about two axes
Maintain illumination of a fixed direction
Only white LED can be used with tracking

## Slide 18: system diagram

## Slide 19: Power subsystem
Milwaukee Red Lithium™ Battery Packs
  Required by Milwaukee Tool
Specifications
  Ranging between 3V and 4V
  Capacity2.0Ah; 10 Wh
Notes: Luckly of us these battery were already tested.

## Slide 20: Microprocessor
Texas Instruments MSP432P401R pack (Development board) was used
  Specifications
    16 bit ARM processor
    Faster and used FPU
    SupplyVoltageRange:1.62V to 3.7 V
    I2C (with multiple-slave addressing)
    Ultra-Low-Power Operating Mode
Notes: 16 bit

## Slide 21: Inertial measurement unit (IMU) with Magnetometer
Critical component to the tracking feature
Provide position and motion changes
Covers x, y and z axes when tracking is enabled

## Slide 22: Specifications
6 axis IMU with Magnetometer
Supply Voltage - 1.2 - 3.6 VDC
Digital interfaces I2C
Gyroscope Sensitivity: The subsystem uses 125°/s
Magnetometer Resolution: 0.3μT, which makes this subsystem very accurate

## Slide 23: Servo motor
Servo motors are going to use data from IMU
Servos will move the white LED to a fix point
2 servos are used
  Vertical
  Horizontal

## Slide 24: How do the servos move?

## Slide 25: Specifications
Operating speed: 0.1 s/60 degree
Operating voltage: 3.2V minimum
  Needs boost converter if motion desired when battery <3.2V
PWM interface
Weight: 3.9 g

## Slide 26: Temperature Sensor
When the temperature is high, the system should shutdown
Specifications
  Operating Voltage 2.5 to 5V
  Digital interface: I2C

## Slide 27: photocell sensor
Auto-brightness: The output brightness automatically adjusts based on ambient light levels
Specifications
  Operating Voltage, VS = 1.6 to 3.6V
  Measurements: 0.01 lux to 83 k lux
  Low Operating Current: 1.8 µA

## Slide 28: Red and white leds
Previous design from Milwaukee Tool chosen for the LED and LED drives
Specifications
  Switchable between Red and White LEDs
  Red LED for manual mode
  White LED for tracking mode
  Red LED is stationary

## Slide 29: integration
Designed finite state machine for tracking algorithm motor controls
Programed to control LED brightness with photocell
Programed pushbuttons to enable to the tracking feature
Mounted the device on a helmet
Ran the system through compliance testing

## Slide 30: price Analysis
New bill of materials will be less expensive
Estimated bulk prices (when ordered part by part in amounts of 5000)
  1. Bosch BMI160 IMU- $2.08 per unit
  2. OPT3001 light sensor- $1.43 per unit
  3. TMP007 temperature sensor- $1.78 per unit
  4. Tower Pro SG-92R DC servomotor – $2.25 per unit
  5. MSP432 Microcontroller - $4.05 per unit
    (Total: $11.59 for these parts)

## Slide 31: Cost analysis
Needs more time in development
  Prototype shows what approaches have failed
  Still uses dev board – no PCB design yet
  Could be offered as a senior design project in 2019
Servomotors have moving parts
  LED dome idea had no gears
  May be more costly implementing dome

## Slide 32: RESULTS
Defining angles of rotation about axes
  Pitch (Theta) – Rotation about y-axis
  Roll (Phi) – Rotation about x-axis
  Yaw (Psi) – Rotation about z-axis

## Slide 33: TEST PLAN AND RESULTS
Basic Diagram of Accelerometer Pitch Test Setup

## Slide 34: RESULTS
Output Acceleration in g's vs Pitch Angle in Degrees

## Slide 35: RESULTS
Accelerometer Pitch Test table and results
Expected Angle, rotation about y-axis Theta (deg) | Experimental Angle rotation about y-axis, Theta (deg) | Experimental Angle rotation about z-axis, Psi (deg)
50 | 48.28 | 0.66
40 | 39.38 | 0.76
30 | 29.64 | 0.85
20 | 20.75 | 0.94
10 | 9.45 | 0.97
0 | 0.43 | 0.99
-10 | -12.49 | -0.97
-20 | -20.73 | -0.93
-30 | -30.82 | -0.85
-40 | -40.76 | -0.77
-50 | -52.8 | -0.66

## Slide 36: RESULTS
Accelerometer and Magnetometer Yaw Test table and results
Expected Angle, Rotation about z-axis Psi (deg) | Experimented Angle Rotation about z-axis, Psi (deg) | Experimented Angle Rotation about y-axis, Theta (deg)
50 | 49.898 | 0.32
40 | 39.635 | 0.32
30 | 30.378 | 0.33
20 | 20.162 | 0.23
10 | 9.947 | 0.26
0 | 0.141 | 0.23
-10 | -10.169 | 0.32
-20 | -21.213 | 0.32
-30 | -30.333 | 0.34
-40 | -38.667 | 0.33
-50 | -48.201 | 0.31

## Slide 37: RESULTS
Combinatorial Pitch Test table and results
Expected Angle, Rotation about y-axis Theta (deg) | Experimented Angle Rotation about y-axis, Theta (deg) | Experimented Angle Rotation about z-axis, Psi (deg)
50 | 48.31 | 74.06
40 | 39.25 | 73.08
30 | 29.56 | 74.26
20 | 20.2 | 73.95
10 | 9.46 | 74.02
0 | 0.33 | 74.02
-10 | -11.2 | 74.35
-20 | -19.61 | 73.98
-30 | -30.03 | 74.10
-40 | -39.64 | 74.12
-50 | -51.78 | 74.16

## Slide 38: RESULTS
Pitch and Yaw values from the combinatorial filter used to move the servomotor and keep the light fixed on the target

## Slide 39: results
Servo angle (degrees) | Pulse Width (ms) [Predicted] | Pulse Width (ms) [Measured]
-90 | 0.52 | 0.52
-50 | 0.90 | 0.90
-40 | 1.00 | 1.00
-30 | 1.10 | 1.10
-20 | 1.20 | 1.20
-10 | 1.30 | 1.30
0 | 1.40 | 1.40
+10 | 1.50 | 1.50
+20 | 1.60 | 1.60
+30 | 1.70 | 1.70
+40 | 1.80 | 1.80
+50 | 1.90 | 1.90
+90 | 2.30 | 2.30
Servo motor demonstration

## Slide 40: Shortcomings
Implementing the auto-shutdown after 5 minutes of no motion
High temperature shutdown function
Power system integration
Headlamp is heavy, yielding slow response from motors
Yaw compensation
  Prone to electromagnetic interference
  Recommend using another approach
  Dr. Kelnhofer suggests a different magnetometer

## Slide 41: Strengths
Dependable pitch compensation
I/O and settings ready for auto-brightness
Motors work as low as 3.2V without boost converter
Devices can be configured to low-power modes
Another prototype could negate most shortcomings
Power consumption can be evaluated without integrating power system
  Best case scenario: 0.66W
  Worst case scenario: 1.37W

## Slide 42: Problems and risks
Lithium batteries raise concern for fire hazards
Safety features built in by Milwaukee Tool's battery management circuit
Must not suffer from structural damage causing the lithium ions to leak
Milwaukee Tool’s hard plastic case protects the battery

## Slide 43: Problems and risks
Tracking algorithm needs better yaw design
Do not give the MSP432 too much voltage
Need to anticipate test failures
Programs and subsystems may need to be redesigned
  Gimbal lock
  Euler angles used - try quaternions

## Slide 44: Questions and answers